## Slide 1
Waste Expo
State of C+I Waste
Mike Ritchie
October 2023

## Slide 2
Chart: Difference compared to 1996/97
| 1996-97 | 1997-98 | 1998-99 | 1999-00 | 2000-01 | 2001-02 | 2002-03 | 2003-04 | 2004-05 | 2005-06 | 2006-07 | 2007-08 | 2008-09 | 2009-10 | 2010-11 | 2011-12 | 2012-13 | 2013-14 | 2014-15 | 2015-16 | 2016-17 | 2017-18 | 2018-19
Population (%) | 0 | 1.002 | 2.1131 | 3.2883 | 4.623 | 5.8199 | 7.0439 | 8.1946 | 9.5196 | 11.008 | 13.0522 | 15.3406 | 17.7425 | 19.5886 | 21.2615 | 23.4462 | 25.6359 | 27.5802 | 29.4621 | 31.6629 | 33.9012 | 36.1775 | 38.4925
Economy (GVA) | 0 | 5.9016 | 12.2068 | 18.1998 | 23.9335 | 31.1522 | 37.1555 | 46.8756 | 55.809 | 65.0503 | 76.887 | 85.1512 | 90.0786 | 96.8811 | 106.5518 | 118.6701 | 127.2628 | 137.5855 | 145.9674 | 155.4417 | 166.5571 | 180.5321 | 190.425
Waste generation (%) | 0 | 5.6742 | 10.8631 | 19.0457 | 21.0414 | 30.5581 | 42.3478 | 53.5719 | 63.4508 | 73.7288 | 89.463 | 97.5162 | 105.3839 | 107.0383 | 109.6769 | 116.7637 | 123.8505 | 130.4853 | 132.9824 | 138.2575 | 139.5191 | 165.512 | 170.3475
Waste generation growth
4.4x population growth
0.9x economic growth
Notes: Excluding fly ash
Source: 2007 Year Book Australia, 2007 & Waste Account, Australia 2010-11, 2014 by ABS
http://www.abs.gov.au/AUSSTATS/abs@.nsf/DetailsPage/1301.02007?OpenDocument http://www.abs.gov.au/ausstats/abs@.nsf/mf/4602.0.55.006
Updated with 2018/19 data. Source: National Waste Report 2020 https://www.environment.gov.au/system/files/pages/5a160ae2-d3a9-480e-9344-4eac42ef9001/files/national-waste-report-2020.pdf Note that resource recovery (which includes EfW, LFG capture and recycling was 63% (43.5Mt recycling + 2.136Mt EfW + LFG).
Economy: IMF data, Australia: Gross domestic product, current prices (Purchasing power parity; international dollars), Data last updated: 09/2019 https://www.imf.org/external/pubs/ft/weo/2019/02/weodata/weorept.aspx?pr.x=69&pr.y=16&sy=1980&ey=2024&scsm=1&ssd=1&sort=country&ds=.&br=1&c=193&s=NGDP_RPCH,PPPGDP,PPPPC,PCPIPCH,LUR,GGXWDG_NGDP&grp=0&a=#cs2

## Slide 3: More waste, more recycling
Chart: Million tonnes
| 1996-97 | 1997-98 | 1998-99 | 1999-00 | 2000-01 | 2001-02 | 2002-03 | 2003-04 | 2004-05 | 2005-06 | 2006-07 | 2007-08 | 2008-09 | 2009-10 | 2010-11 | 2011-12 | 2012-13 | 2013-14 | 2014-15 | 2015-16 | 2016-17 | 2017-18 | 2018-19
Waste generation | 22.7485 | 24.0393 | 25.2197 | 27.0811 | 27.5351 | 29.7 | 32.382 | 34.9353 | 37.1826 | 39.5207 | 43.1 | 46.7218 | 47.0981 | 47.6983 | 52.432 | 53 | 54.487 | 61.5
Waste disposal | 21.2205 | 17.423 | 19.1995 | 21.2008 | 19.8664 | 18.6628 | 19.9745 | 20.8514 | 19.976 | 27.2
Waste recycling | 1.528 | 14.959 | 22.5746 | 24.0434 | 25.5124 | 27.0694 | 29.5693 | 29.8554 | 31.715 | 43.5
Energy recovery | 1.368 | 1.4776 | 1.7193 | 1.9661 | 2.8882 | 2.3113 | 1.973 | 2.14
Notes: Updated with 2018/19 data. Source: National Waste Report 2020 https://www.environment.gov.au/system/files/pages/5a160ae2-d3a9-480e-9344-4eac42ef9001/files/national-waste-report-2020.pdf

## Slide 5: To hit 80% diversion - Target
Chart: Million tonnes
| 1996-97 | 1997-98 | 1998-99 | 1999-00 | 2000-01 | 2001-02 | 2002-03 | 2003-04 | 2004-05 | 2005-06 | 2006-07 | 2007-08 | 2008-09 | 2009-10 | 2010-11 | 2011-12 | 2012-13 | 2013-14 | 2014-15 | 2015-16 | 2016-17 | 2017-18 | 2018-19
Waste generation | 22.7485 | 24.0393 | 25.2197 | 27.0811 | 27.5351 | 29.7 | 32.382 | 34.9353 | 37.1826 | 39.5207 | 43.1 | 46.7218 | 47.0981 | 47.6983 | 52.432 | 53 | 54.487 | 61.5
Waste disposal | 21.2205 | 17.423 | 19.1995 | 21.2008 | 19.8664 | 18.6628 | 19.9745 | 20.8514 | 19.976 | 27.2
Waste recycling | 1.528 | 14.959 | 22.5746 | 24.0434 | 25.5124 | 27.0694 | 29.5693 | 29.8554 | 31.715 | 43.5
Energy recovery | 1.368 | 1.4776 | 1.7193 | 1.9661 | 2.8882 | 2.3113 | 1.973 | 2.14
Notes: Updated with 2018/19 data. Source: National Waste Report 2020 https://www.environment.gov.au/system/files/pages/5a160ae2-d3a9-480e-9344-4eac42ef9001/files/national-waste-report-2020.pdf

## Slide 6
Chart: Australia - National Waste Report
| 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Waste Generated | 48.41 | 50.88 | 51.83 | 51.86 | 52.9 | 53.61 | 54.82 | 57.26 | 60.43 | 61.54
Waste Recycled | 24.72 | 26.1 | 27.58 | 29.17 | 29.85 | 30.67 | 31.98 | 33.62 | 36.12 | 37.58
Waste Disposed | 21.26 | 22.37 | 21.85 | 20.11 | 19.84 | 19.66 | 19.71 | 20.7 | 20.96 | 20.6
Energy Recovery | 1.822 | 1.851 | 1.778 | 1.898 | 2.334 | 2.428 | 2.302 | 2.143 | 2.156 | 2.135
Recycling Goal | 56.0261
Disposal Goal | 14.0065
Notes: Excluding fly ash
Note that 61.5Mt> 43.5+27.2. The balance is energy recovery.
Source: 2007 Year Book Australia, 2007 & Waste Account, Australia 2010-11, 2014 by ABS
http://www.abs.gov.au/AUSSTATS/abs@.nsf/DetailsPage/1301.02007?OpenDocument http://www.abs.gov.au/ausstats/abs@.nsf/mf/4602.0.55.006
Updated with 2018/19 data. Source: National Waste Report 2020 https://www.environment.gov.au/system/files/pages/5a160ae2-d3a9-480e-9344-4eac42ef9001/files/national-waste-report-2020.pdf Note that resource recovery (which includes EfW, LFG capture and recycling was 63% (43.5Mt recycling + 2.136Mt EfW + LFG).

## Slide 7
Source: ABS Year Book 2014; National Waste Report 2018
* The balance of landfilled/recycled is waste recovered as energy, including via LFG.
Generation
22.7 Mt
21.2 Mt Landfill
1996
Recycling 1.5 Mt
Recovery 1.5 Mt
Generation
64 Mt
~23 Mt Landfill*
2022
Recycling 40 Mt
7%
60%
New National Target - 80% by 2030
Another
18 MT/yr recycled by 2030
Waste Generation
Notes: Excluding fly ash
Note that 61.5Mt> 43.5+27.2. The balance is energy recovery.
Source: 2007 Year Book Australia, 2007 & Waste Account, Australia 2010-11, 2014 by ABS
http://www.abs.gov.au/AUSSTATS/abs@.nsf/DetailsPage/1301.02007?OpenDocument http://www.abs.gov.au/ausstats/abs@.nsf/mf/4602.0.55.006
Updated with 2018/19 data. Source: National Waste Report 2020 https://www.environment.gov.au/system/files/pages/5a160ae2-d3a9-480e-9344-4eac42ef9001/files/national-waste-report-2020.pdf Note that resource recovery (which includes EfW, LFG capture and recycling was 63% (43.5Mt recycling + 2.136Mt EfW + LFG).

## Slide 8
Source: ABS Year Book 2014; National Waste Report 2018
* The balance of landfilled/recycled is waste recovered as energy, including via LFG.
Generation
22.7 Mt
21.2 Mt Landfill
1996
Recycling 1.5 Mt
Recovery 1.5 Mt
Generation
70Mt
14 Mt Landfill*
2030
Recycling 56 Mt
7%
80%
By 2030
18 MT/yr growth in 10 years
Notes: Excluding fly ash
Note that 54.5Mt> 31.7+21.7. The balance is energy recovery.
Source: 2007 Year Book Australia, 2007 & Waste Account, Australia 2010-11, 2014 by ABS
http://www.abs.gov.au/AUSSTATS/abs@.nsf/DetailsPage/1301.02007?OpenDocument http://www.abs.gov.au/ausstats/abs@.nsf/mf/4602.0.55.006
Updated with 2016/17 data. Source: National Waste Report 2018 https://www.environment.gov.au/system/files/resources/7381c1de-31d0-429b-912c-91a6dbc83af7/files/national-waste-report-2018.pdf Note that resource recovery (which includes EfW, LFG capture and recycling was 62% (31.7Mt recycling + 1.973Mt EfW + LFG).

## Slide 9: What we landfill and recycle
Tyres: 0.17 (56%)
Paint : 0.03 (15%)
Oil: 0.69 Mt
Landfill
64 Mt
core waste generated
Plastics: 0.34 (15%)
8.7Mt Mixed C+I
7.5 Organics
6.5 Mixed C+D
2.2 Plastics
0.7 Textiles
0.7 Metals
0.3 Tyres
0.2 Paint
0.0008
Coffee cups
Tonnages based on:
- Core waste data from National Waste Report 2022.
- *BioPak 2018
23 Mt
Metals: 4.8 Mt
Organics: 7.8 Mt
Masonry: 16.0 Mt
Mattresses: 0.02
Notes: critically review myths (plastic bag) and decide on priority streams based on bang for $ (s 46-47)

## Slide 10: Davis Rd

## Slide 11: Davis Rd

## Slide 12: Victoria – 2.1 MT new C+I recycling to hit target
Chart: Vic C&I Waste
| 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Generated | 5.2667 | 5.0258 | 5.0833 | 5.3184 | 5.3603 | 5.1536 | 5.3977 | 5.7376 | 6.2839 | 6.1907 | 5.9094 | 5.9513
Recycled | 2.7404 | 2.6407 | 2.9353 | 3.1013 | 3.4594 | 3.3764 | 3.552 | 3.8258 | 3.9936 | 3.809 | 3.2733 | 3.2766
Disposed | 2.146 | 1.9943 | 1.756 | 1.8228 | 1.5428 | 1.5725 | 1.6807 | 1.8014 | 2.0966 | 2.1594 | 2.2726 | 2.3146
Recycling Goal | 5.3946
Landfill Goal | 1.3486

## Slide 13
Chart: QLD C&I Waste
| 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Generated | 3.7971 | 3.7639 | 3.6084 | 3.5853 | 4.4971 | 4.4528 | 4.0934 | 4.3711 | 4.4925 | 4.7959 | 4.0836 | 4.4676
Recycled | 1.9461 | 1.8839 | 1.7745 | 1.8952 | 2.3538 | 2.3301 | 2.072 | 2.2586 | 2.3539 | 2.6392 | 2.0988 | 2.2854
Disposed | 1.6696 | 1.7229 | 1.6657 | 1.504 | 2.0031 | 1.9915 | 1.9136 | 2.0154 | 2.0417 | 2.0658 | 1.7654 | 2.03
Recycling Goal | 4.1419
Landfill Goal | 1.0355
QLD 1.8 MT

## Slide 14
Chart: NSW C&I Waste
| 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Generated | 5.5401 | 6.493 | 6.4884 | 6.3617 | 6.3032 | 6.205 | 6.2319 | 6.1004 | 5.4036 | 5.5829 | 5.7565 | 5.4585
Recycled | 2.8496 | 3.402 | 3.7609 | 3.6875 | 3.4778 | 3.4515 | 3.1512 | 2.8413 | 2.6001 | 2.5204 | 2.9 | 2.6932
Disposed | 2.4661 | 2.8611 | 2.4785 | 2.4618 | 2.5378 | 2.5264 | 2.808 | 3.0062 | 2.4991 | 2.7142 | 2.7308 | 2.6303
Recycling Goal | 4.2182
Landfill Goal | 1.0545
NSW 1.5 MT

## Slide 15: 8.5 MT being landfilled 6.25 MT – Vic, QLD, NSW, WA alone to hit targets
Chart: WA C&I Waste
| 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Generated | 2.3682 | 2.0108 | 2.5122 | 2.1549 | 2.4667 | 2.0651 | 2.2494 | 2.0996 | 2.385 | 2.3475 | 2.4399 | 2.4727
Recycled | 1.1846 | 0.77219 | 0.9816 | 0.96244 | 1.3102 | 1.2082 | 1.1991 | 1.1153 | 1.2278 | 1.2643 | 1.2643 | 1.212
Disposed | 1.1405 | 1.1926 | 1.4807 | 1.1331 | 1.0718 | 0.74222 | 0.90737 | 0.90573 | 1.0157 | 0.93675 | 1.0682 | 1.1191
Recycling Goal | 1.9571
Landfill Goal | 0.48928
WA 0.7 MT

## Slide 16
Waste is like a river - it flows downhill to the cheapest price
Most recycling is uneconomic – subsidised by you
Organics are the biggest stream but uneconomic to recycle compared to under-priced landfill
To hit 80% government targets
  Better recycling
  Properly priced landfills
  FOGO/ COFO collections
  EfW
Economic principles of Waste

## Slide 17
1. Landfill levies drive recycling
2. Source separation
3. Sorting infrastructure
4. EPR schemes
5. Weight based billing
6. Circular economy interventions
7. Efw
How do we lift C+I recycling?

## Slide 18
  1. Landfill Levies
Chart: Levy ($/t)
| 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2022 | 2023
NSW (Metropolitan Levy Area) | 19.2 | 19.2 | 19.8 | 22.8 | 29.7 | 46.7 | 58.8 | 70.3 | 82.2 | 95.2 | 107.8 | 120.9 | 133.1 | 135.7 | 138.2 | 141.2 | 143.6 | 146
NSW projected (Metropolitan Levy Area) | 146 | 150.38 | 154.8914 | 159.5381
Vic (metro) | 3 | 3 | 3 | 6 | 7 | 8 | 9 | 30 | 44 | 48.4 | 53.2 | 58.5 | 60.7 | 62.033 | 63.28 | 64.3 | 65.9 | 65.9 | 105.9 | 125.9 | 129.677
Vic projected (metro) | 129.677
SA (metro) | 10.1 | 10.5 | 10.8 | 11.2 | 23.4 | 24.2 | 25.2 | 26 | 35 | 42 | 47 | 52 | 57 | 76 | 87 | 100 | 110 | 140 | 144.2
SA projected (metro) | 144.2 | 148.526 | 152.9818
WA (metro) | 3 | 3 | 6 | 6 | 7 | 7 | 28 | 28 | 28 | 28 | 28 | 55 | 55 | 60 | 65 | 70 | 70 | 70 | 72.1
WA projected (metro) | 72.1 | 74.263 | 76.4909
Qld | 35 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 70 | 75 | 80
QLD projected | 80 | 85 | 90 | 95
Tas
Notes: Emphasising issues with underpriced landfills

## Slide 19: Levies – shift the inflection point
Diversion rate from landfill
Cost per tonne ($)
Plastic bags
Fluoro tubes
batteries
Textiles
Organics- Food waste, Manure
Metals
cardboard
Concrete
E waste
Hard Plastics
Mattress
CD’s
Wood
Glass
Returned food
Butts
High $ Value
Large Tonnage
Rising
levies
$0 /t
$1000/t

## Slide 20
2. Source separation
Get the price signals right
Educate
Drive separation for:
  Food
  Cardboard
  Plastics
  Polystyrene
  Green waste
  Steel
  Aluminum
NSW Govt Mandate (above a size threshold) – must have a COFO collection by 2025
  Supermarkets
  Retail
  Institutions
  Food manufactures

## Slide 21: 3. Sorting infrastructure – Dirty MRFs
Only 2 in Sydney - 70kt out of 8.5 MT being landfilled;
  some C+D facilities blending C+I waste in
The reason is economics
  Cheaper to landfill mixed C+I than separate and recycle
  Contaminated by food waste and liquids
  Recoverable materials ~ 40% of stream (cf C+D at 80%)
Gate fee $300 /t
Sorting $150 /t
38% Sales:
Basket of goods ~ $123
62% Landfill: -$320

## Slide 22
C+I Dirty MRF

## Slide 23: 4 EPR, CDS, Plastic packaging
EPR proposed List
  Textiles
  Soft plastic
  Ag plastic
  PVC
  Furniture
  Refrigerators
  Air conditioners
  Bedding
  Plant pots
  Batteries
  Dairy silage
  Nappies
  Sports equipment and shoes
  Cosmetics
  Cups
  Coffee pods
  Bikes
  Car seats
18%






2023


2023
CDS
Current EPR is weak
  CDS, Tyres and Oil making a difference
  Rest are capturing a small %
Recycling and Waste Reduction Act 2020 (Federal)
  Needs to be used
  Made mandatory
  Ban non-recyclable products

## Slide 24: 5. Weight Based Billing
Volume based charging – weak price signal
WBB – pay for the weight in the bin:
  more aware of the true cost
  adjust behaviour with immediate savings
45% reduction in waste to landfill in UK
Most C+I is volume based billing
C&D is already weight based
$/m
Waste contractors -assume a density to determine disposal cost and to calculate the lift rate

## Slide 25: 6. Circular Economy - Pragmatic steps
Economy
Must haves:
Design for reuse and recycling rules
Recycling labelling rules
Recycled content rules
Extended Producer Scheme rules
Reuse/ Recycling
Must haves:
Economics to drive recycling
Collection systems esp. organics
Landfill levies and bans
Govt procurement rules
Planning for infrastructure
Supply chain restructure
Design
Broken at both ends

## Slide 26
  7. Energy from Waste
QLD – 1
ResourceCo Hemmant $50m 150kt
Remondis
NSW – 3 ?
Reg Growth- Parkes - 400kt
Veolia- Woodlawn - 400kt
Richmond Valley - ?
TNG Sydney – Eastern Ck
Suez Sydney - Botany
Cleanaway Sydney – Eastern Ck
Re.Group Lithgow
CWY Greenspot Wallerawang- Lithgow
Jerrara Goulburn
VIC – 4
Opal - 350kt
Sims – 150kt
GSWT - 150kt
REA – 150kt
1 MT CAP
WA – 2
Kwinana – Veolia 400kt
East Rockingham - Veolia 400kt
Notes: Source: EPA data provided for WLRM 2 Justification Project

## Slide 27
Conclusions
We have no chance of hitting the C+I Targets without government action
Any combination of these actions will accelerate reform:
  Landfill levies
  Source separation
  Sorting infrastructure
  EPR schemes
  Weight based billing
  Circular economy interventions
  Efw

## Slide 28
Thank you
MRA Consulting Group
Suite 408 Henry Lawson Building?19 Roseby Street Drummoyne NSW 2047
P 02 8541 6169?
info@mraconsulting.com.au
mraconsulting.com.au
MRA services:
Strategy
Commercial
Circular economy
Planning
Auditing
Carbon and emissions
Engineering
Procurement
Advocacy